Telcom 2720 Cellular and Wireless Networks

Homework 2                                                       Spring 08

- Briefly describe the difference between the following

(a) Fast and Slow Fading

(b) Shadowing and Diffraction

(c) Antenna Gain in dBi and dBd

- Suppose the maximum fade duration over a radio channel is 0.001 ms. Assume that all the bits are in error when a signal encounters a fade. What is the maximum  number of consecutive bits that are in error for a transmission through this channel if the data rate is 10Kbps? If the data rate is 11 Mbps?

- Block interleaving is a solution to enable simple error correcting codes to correct long bursts of errors. For both the situations in problem 1 (a) determine the number of  codewords over which interleaving has to be performed in the length of the codeword is 7 bits  and a single bit error can be corrected (b) determine the interleaving delay

- Consider a  cellular system that uses frequency hopping and has 124 frequency channels of spectrum. Below is the hopping pattern for a user in a cell that has 31 frequency channels assigned to it. (a) Is the hopping pattern random or cyclic? (b) is this a slow or fast frequency hopping system? Why?

| Time slot | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Input data | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 |
| Frequency | f1 | f3 | f27 | f28 | f110 | f16 |

| Time slot | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Input data | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 0 |
| Frequency | f11 | f3 | f2 | f14 |

- Consider the simple CDMA example of Bob and Alice in class Slides 3. Show that given the combined received signal (below), by using Bob’s code of [1, 1] to despread the signal  Bob can recover the information sent to him by the base station.