Telcom 2720 Cellular and Wireless Networks      Homework  7  Spring 2008

- List the entities of mobile IP and describe data transfer from a mobile node to a fixed node and vice versa. Why and where is encapsulation needed?

- What are the basic differences between wireless WANs and WLANs, and what are the common features? Consider mode of operation, administration, frequencies, capabilities of nodes, services, national/international regulations.

- Name major transmission techniques considered for WLAN standards and give the IEEE standard activity associated with each of them.

- What is the difference between an ESS and a BSS in the IEEE 802.11?

- What is the difference between a probe and a beacon signal in 802.11?

- Consider a WLAN AP that operates at 100mW in the 2.4 GHz band on the ceiling of  8th floor of a  office building. Using the JTC model determine if the WLAN can be accessed  1 meter off the floor on the 4th floor of the building  while directly beneath the AP. Each floor is 3 meters distance and the WLAN access card requires –80dBm signal strength.